## Slide 1: An open source software package to compare and extend effective mass models of the phosphorus donor in silicon
Presentation Date: Monday, March 6, 2023 4:36 pm
Luke Pendo and Xuedong Hu
We thank financial support by US ARO via grant W911NF1710257.
gitlab.com/cantankerous-impurity

## Slide 2: Our PrOBlem

## Slide 3
Original crystal structure picture by Ben Mills, public domain.
https://commons.wikimedia.org/w/index.php?curid=2722584
Modified by L. Pendo for presentation.
System description
Infinite silicon crystal bulk.
One silicon replaced by an isolated pnictogen (Series V/Group 15).
Specifically we consider the phosphorous substitutional donor.
System is symmetric about the impurity under operations of point group Td.
Excess electric charge of phosphorous nuclear attracts excess electron.
P
The back of the envelope idea
Excess electron is affected by a periodic mean field potential, and weakly bound to donor potential.
  Short-range: looks like a Bloch wave.
  Long-range: attenuated on a radial scale much longer then lattice parameter.

## Slide 4: The Model

## Slide 5: The effective mass approximation
EMA: Assume the donor electron is localized in k-space at the six-fold degenerate minima of the silicon conduction band.
  Short-range: Bloch wave.
  Long-range: Envelope function.
We expand the envelope function with a set of basis functions.

## Slide 6: The Generalized Eigenvalue Problem
“Modified” Shindo-Nara effective mass equation[1] cast as a generalized eigenvalue problem[2].
[1] K. Shindo and H. Nara, J. Phys. Soc. Jpn. 40, 1640 (1970)
[2] J. K. Gamble et al., Phys. Rev. B 91, 235318 (2015)
symmetrized anisotropic basis states
U is intended to model all deviations from the pure silicon potential.
H0 is intended to model the pure silicon potential.
Bloch functions of opposed valley minima are included as Fourier series:

## Slide 7: Matrix Construction – Overlap, Hamiltonian

## Slide 8: Views on the effective mass approximation
[1] R.A. Faulkner, Phys. Rev. 184, 713 (1969)
[2] A.K. Ramdas and S. Rogriguez, Rep Prog Phys. 44, 1297 (1981)
An attractively intuitive physical picture of the state of the donor electron.
Less computationally expensive as compared to ab initio and tight-binding models.
Predicts the energies of spatially extended excited states of donors [1,2].
Struggles to present a quantitively persuasive picture of the ground state manifold
Few agreed upon criteria for refutability (beyond agreement with energy spectrum).
Lots of freedom to generate different schemes through reasonable but ad hoc assumptions.
Is further improvement of effective mass methods possible?
Notes: For the authors, it remains an open question if these difficulties can be resolved by incorporating additional phenomenological corrections or if they are evidence of a more fundamental breakdown of the effective mass approximation itself.

## Slide 9: Model evaluation
Verisimilitude
How well does the model resemble reality?
Out of model
Consistency
How well does the model play by its own rules?
Completeness
Can the model answer questions posed to it?
In-model
Background
[*] arXiv:2302.04919
V-score[*]: Metric for model completeness
Is the trial eigenstate well-converged to an actual eigenstate?

## Slide 10: “Modified” Shindo-Nara equation?
It is a reasonable assumption for verisimilitude that the kinetic term doesn’t mix the valleys.
However, to ensure that the square of the V-score is positive definite, the previously dropped terms must be kept.

## Slide 11: Matrix Construction – Hamiltonian Squared

## Slide 12: The Basis

## Slide 13: Naïve basis functions defined

## Slide 14: Complete, Extensible “Subbasis”
Underlying naïve subbases are orthonormal, fully complete over .
Solid angle expansion in spherical harmonics. Radial expansion in Laguerre polynomials.
Basis can utilize Slater (“hydrogen-like”) or Gaussian (“harmonic oscillator”) exponential decay.
Variational tuning: anisotropy along azimuth, overall radial scaling.
Bloch functions of valley minima are included as Fourier series.
Users can freely select size, composition of each subbasis.

## Slide 15: “Superbasis”
Difficult to optimize an orthonormal, complete basis span over multiple energy eigenstates.
This can be resolved by using a basis constructed as a concatenation of multiple subbases.
Superbasis formed from multiple orthonormal subbases individually equipped with tuning parameters.
Superbasis is non-orthonormal, overcomplete on .
Optimization of each subbasis seems to greatly reduce numerical effects from overcomplete basis.
Total number and size of subbases limited only by computation limits.
Work on-going to increase code efficiency to allow for larger sub- and super-bases.

## Slide 16: Complete, Extensible Basis
Representation of single eigenstate
Underlying naïve subbases are orthonormal, fully complete over .
Two variational parameters: anisotropy along azimuth, overall radial scaling.
Users can select membership and size of each subbasis.
However, difficult to optimize subbasis to span over multiple energy eigenstates.
Representation of multiple eigenstates / energy spectra
Superbasis concatenation of individual independent subbases.
Superbasis non-orthonormal, overcomplete on .
Optimization of each subbasis seems to mitigate problems from overcompleteness.
Total number and composition of subbases limited ONLY by computation limits.
Work on-going to increase code efficiency to allow for larger sub- and super-bases.

## Slide 17: Generalized basis states -- I

## Slide 18: Generalized basis states -- II

## Slide 19: The SYMMETRY

## Slide 20: Symmetry considerations
States with m even are indexed by inversion (ω) and acyclic (σ) symmetry.
States with m odd are indexed by acyclic (σ) symmetry and a free index (h).
m odd states only have odd inversion.

## Slide 21: Effect of Td operations, including Bloch functions, m even
Double inversion
Time-reversal
States indexed by inversion (ω) and acyclic (σ) symmetry as either even (+1) or odd (-1)
Cyclic permutations
Acyclic permutations

## Slide 22: Effect of Td operations, including Bloch functions, m odd
States indexed by acyclic (σ) symmetry as either even (+1) or odd (-1). m odd states have odd inversion (ω = -1).
Double inversion
Time-reversal
Cyclic permutations
Acyclic permutations

## Slide 23: Full Accounting of Symmetry, Basis
Multi-valley basis functions are symmetrized according to Td symmetry of silicon.
Forms for A2 and T1 are also known.
Selection rules for all symmetries are analytically known, but have not yet been implemented in code.

## Slide 24: POTENTIAL Model

## Slide 25: Flexible Potential Model
The fraktur constants can be freely set by users of the software.
Potential form represents most extant models of the effective silicon donor potential.
Examples include the tetrahedral potential used by Gamble [1] and the dynamic dielectric model [2,3].
To facilitate deep exploration, a very general potential model.
[1] J.K. Gamble et al., Phys. Rev. B 91, 235318 (2015)
[2] A.Q. Sarker, J. Phys. C 10 2617 (1977)
[3] M. Usman, et al., J. Phys.:Condens. Matter 27 154207 (2015)

## Slide 26: Test Case
Single-Valley Wavefunctions
Beyond Kohn-Luttinger

## Slide 27: Kohn-Luttinger (Historic)
Basis(m,l,k)
0,0,0

## Slide 28: Expanded Single-Valley
Basis(m,l,k)
0,0,0
0,0,1
0,0,2
0,0,3
0,2,0
0,2,1
0,2,2
0,2,3
0,4,0
0,4,1
0,4,2
0,4,3
0,6,0
0,6,1
0,6,2
0,6,3

## Slide 29: Conclusions

## Slide 30: Caveats and Challenges -- I
Precalculations
Complete basis requires computation of alternating sign sums – floating point computation unstable.
Alternating sign computations performed symbolically with python module Sympy.
Results stored in SQLite database; retrieved at runtime.
Symbolic precalculation takes substantial time, but a one-time investment.
Database Access
Size of the precalculation SQLite database on the order of GBs.
Network distribution difficult. User assumes computation and storage responsibilities.
Importation into runtime memory presents a recurring bottleneck.

## Slide 31: Caveats and Challenges -- II
Parameter Optimization
Variational tuning of subbases currently requires hand-tuning.
Superbasis concept introduces large multi-dimensional variational space, requires stochastic search.
Earlier proof of concept in Fortran implemented an Artificial Bee Colony stochastic optimization algorithm.
Working on integrating extant ABC code within current incarnation of project.
Numerical Stability and Verisimilitude
Computations involve numerical matrix and cubature methods.
Some regions of parameter space seem “sour”/“unstable” leading to unreliable or unbelievable results.
Multi-valley overlap, kinetic elements necessary for completeness and consistency, but detracts from verisimilitude.
Working on expanding unit testing of code, as well as runtime monitors for numerical stability.
Working on runtime analysis on breakdown and deviations from the EMA.

## Slide 32: Prospects
https://gitlab.com/cantankerous-impurity
Specific focus of my PhD research on Si:P and the EMA, but framework is very general.
Want to make code and documentation available as an open science, open notes, open source GPL 3 licensed project.
Can be used to explore other Hamiltonians, other symmetries, other systems.
Extensions
Perturbations of Td symmetry.
External fields, electric, magnetic.
Multi-center effects.
Multi-electron effects.
Forks
Different donors in silicon.
Different bulk materials.
2-D systems: quantum dots.

## Slide 33: “The Pitch”
https://gitlab.com/cantankerous-impurity
Opportunity for a collaboration led by PhD students, postdocs, early career scientists.
A chance to develop scientific, technical, logistic, communication, and management skills.
  Python: Symbolic computations, data analysis, data visualization, SQL integration.
  C++: Code analysis, optimization, documentation. Work with new features of latest C++ standard.
  Fortran: Integration of scientific code from multiple languages.
  Mathematics: Symmetry group theory. Numerical stability. Stochastic optimization. Function representation.
Upshot: Want others to benefit from 10,000+ lines of code, thousands of work hours.
Interested?
E-mail: lukepend@buffalo.edu, luke.pendo@gmail.com
Gitlab repo: cantankerous-impurity